## Slide 1: Medium Access Control Sublayer

## Slide 2: Introduction
In broadcast networks, several stations share a single communication channel.
The major issue in these networks is, which station should transmit data at a given time.
This process of deciding the turn of different stations is known as Channel Allocation.
To coordinate the access to the channel, multiple access protocols are required.
All these protocols belong to the MAC sublayer.

## Slide 3: Introduction
Data Link layer is divided into two sublayers:
  Logical Link Control (LLC)
  Medium Access Control (MAC)
LCC is responsible for error control & flow control.
MAC is responsible for multiple access resolutions.
Network Layer
Logical Link Control (LLC)
Medium Access Control (MAC)
Physical Layer
Data Link Layer

## Slide 4: Channel Allocation Problem
In broadcast networks, single channel is shared by several stations.
This channel can be allocated to only one transmitting user at a time.
There are two different methods of channel allocations:
  Static Channel Allocation
  Dynamic Channel Allocation

## Slide 5: Static Channel Allocations
In this method, a single channel is divided among various users either on the basis of frequency or on the basis of time.
It either uses FDM (Frequency Division Multiplexing) or TDM (Time Division Multiplexing).
In FDM, fixed frequency is assigned to each user, whereas, in TDM, fixed time slot is assigned to each user.

## Slide 6: Dynamic Channel Allocation
In this method, no user is assigned fixed frequency or fixed time slot.
All users are dynamically assigned frequency or time slot, depending upon the requirements of the user.

## Slide 7: Multiple Access Protocols
Many protocols have been defined to handle the access to shared link.
These protocols are organized in three different groups.:
  Random Access Protocols
  Controlled Access Protocols
  Channelization Protocols

## Slide 8: Multiple Access Protocols
Random Access Protocols
ALOHA
Pure ALOHA
Slotted ALOHA
CSMA
1-
Persistent
Non- Persistent
P-
Persistent
CSMA/CD
CSMA/CA
Controlled Access Protocols
Reservation
Polling
Token Passing
Channelization Protocols
FDMA
TDMA
CDMA

## Slide 9: Random Access Protocols
It is also called Contention Method.
In this method, there is no control station.
Any station can send the data.
The station can make a decision on whether or not to send data. This decision depends on the state of the channel, i.e. channel is busy or idle.
There is no scheduled time for a stations to transmit.
They can transmit in random order.

## Slide 10: Random Access Protocols
There is no rule that decides which station should send next.
If two stations transmit at the same time, there is collision and the frames are lost.
The various random access methods are:
  ALOHA
  CSMA (Carrier Sense Multiple Access)
  CSMA/CD (Carrier Sense Multiple Access with Collision Detection)
  CSMA/CA (Carrier Sense Multiple Access with Collision Avoidance)

## Slide 11: ALOHA
ALOHA was developed at University of Hawaii in early 1970s by Norman Abramson.
It was used for ground based radio broadcasting.
In this method, stations share a common channel.
When two stations transmit simultaneously, collision occurs and frames are lost.
There are two different versions of ALOHA:
  Pure ALOHA
  Slotted ALOHA

## Slide 12: Pure ALOHA
In pure ALOHA, stations transmit frames whenever they have data to send.
When two stations transmit simultaneously, there is collision and frames are lost.
In pure ALOHA, whenever any station transmits a frame, it expects an acknowledgement from the receiver.
If acknowledgement is not received within specified time, the station assumes that the frame has been lost.

## Slide 13: Pure ALOHA
If the frame is lost, station waits for a random amount of time and sends it again.
This waiting time must be random, otherwise, same frames will collide again and again.
Whenever two frames try to occupy the channel at the same time, there will be collision and both the frames will be lost.
If first bit of a new frame overlaps with the last bit of a frame almost finished, both frames will be lost and both will have to be retransmitted.

## Slide 14: Pure ALOHA

## Slide 15: Slotted ALOHA
Slotted ALOHA was invented to improve the efficiency of pure ALOHA.
In slotted ALOHA, time of the channel is divided into intervals called slots.
The station can send a frame only at the beginning of the
slot and only one frame is sent in each slot.
If any station is not able to place the frame onto the channel at the beginning of the slot, it has to wait until the next time slot.
There is still a possibility of collision if two stations try to send at the beginning of the same time slot.

## Slide 16: Slotted ALOHA

## Slide 17: Carrier Sense Multiple Access (CSMA)
CSMA was developed to overcome the problems of ALOHA i.e. to minimize the chances of collision.
CSMA is based on the principle of “carrier sense”.
The station sense the carrier or channel before transmitting a frame.
It means the station checks whether the channel is idle or busy.
The chances of collision reduces to a great extent if a station checks the channel before trying to use it.

## Slide 18: Carrier Sense Multiple Access (CSMA)

## Slide 19: Carrier Sense Multiple Access (CSMA)
The chances of collision still exists because of propagation delay.
The frame transmitted by one station takes some time to reach the other station.
In the meantime, other station may sense the channel to be idle and transmit its frames.
This results in the collision.

## Slide 20: Carrier Sense Multiple Access (CSMA)
There are three different types of CSMA protocols:
  1-Persistent CSMA
  Non-Persistent CSMA
  P-Persistent CSMA

## Slide 21: 1-Persistent CSMA
In this method, station that wants to transmit data, continuously senses the channel to check whether he channel is idle or busy.
If the channel is busy, station waits until it becomes idle.
When the station detects an idle channel, it immediately transmits the frame.
This method has the highest chance of collision because two or more stations may find channel to be idle at the same time and transmit their frames.

## Slide 22: Non-Persistent CSMA
A station that has a frame to send, senses the channel.
If the channel is idle, it sends immediately.
If the channel is busy, it waits a random amount of time and then senses the channel again.
It reduces the chance of collision because the stations wait for a random amount of time .
It is unlikely that two or more stations will wait for the same amount of time and will retransmit at the same time.

## Slide 23: P-Persistent CSMA
In this method, the channel has time slots such that the time slot duration is equal to or greater than the maximum propagation delay time.
When a station is ready to send, it senses the channel.
If the channel is busy, station waits until next slot.
If the channel is idle, it transmits the frame.
It reduces the chance of collision and improves the efficiency of the network.

## Slide 24: CSMA with Collision Detection (CSMA/CD)
In this protocol, the station senses the channel before transmitting the frame. If the channel is busy, the station waits.
Additional feature in CSMA/CD is that the stations can detect collisions.
The stations abort their transmission as soon as they detect collision.
This feature is not present in CSMA.
The stations continue to transmit even though they find that collision has occurred.

## Slide 25: CSMA with Collision Detection (CSMA/CD)

## Slide 26: CSMA with Collision Detection (CSMA/CD)
In CSMA/CD, the station that sends its data on the channel, continues to sense the channel even after data transmission.
If collision is detected, the station aborts its transmission and waits for a random amount of time & sends its data again.
As soon as a collision is detected, the transmitting station release a jam signal.
Jam signal alerts other stations. Stations are not supposed to transmit immediately after the collision has occurred.

## Slide 27: CSMA with Collision Avoidance (CSMA/CA)
This protocol is used in wireless networks because they cannot detect the collision.
So, the only solution is collision avoidance.
It avoids the collision by using three basic techniques:
  Interframe Space
  Contention Window
  Acknowledgements

## Slide 28: CSMA with Collision Avoidance (CSMA/CA)

## Slide 29: Interframe Space
Whenever the channel is found idle, the station does not transmit immediately.
It waits for a period of time called Interframe Space (IFS).
When channel is sensed idle, it may be possible that some distant station may have already started transmitting.
Therefore, the purpose of IFS time is to allow this transmitted signal to reach its destination.
If after this IFS time, channel is still idle, the station can send the frames.

## Slide 30: Contention Window
Contention window is the amount of time divided into slots.
Station that is ready to send chooses a random number of slots as its waiting time.
The number of slots in the window changes with time.
It means that it is set of one slot for the first time, and then doubles each time the station cannot detect an idle channel after the IFS time.
In contention window, the station needs to sense the channel after each time slot.

## Slide 31: Acknowledgment
Despite all the precautions, collisions may occur and destroy the data.
Positive acknowledgement and the time-out timer helps guarantee that the receiver has received the frame.

## Slide 32: Controlled Access Protocol
In this method, the stations consult each other to find which station has a right to send.
A station cannot send unless it has been authorized by other station.
The different controlled access methods are:
  Reservation
  Polling
  Token Passing

## Slide 33: Reservation
In this method, a station needs to make a reservation before
sending data.
The time is divided into intervals. In each interval, a reservation frame precedes the data frames sent in that interval.
If there are N stations, then there are exactly N reservation slots in the reservation frame.
Each slot belongs to a station.
When a station needs to send a frame, it makes a reservation in its own slot.
The stations that have made reservations can send their
frames after the reservation frame.

## Slide 34: Polling
Polling method works in those networks where primary and secondary stations exist.
All data exchanges are made through primary device even when the final destination is a secondary device.
Primary device controls the link and secondary device follow the instructions.

## Slide 35: Token Passing
Token passing method is used in those networks where the stations are organized in a logical ring.
In such networks, a special packet called token is circulated
through the ring.
Station that possesses the token has the right to access the channel.
Whenever any station has some data to send, it waits for the token. It transmits data only after it gets the possession of token.
After transmitting the data, the station releases the token and
passes it to the next station in th ring.
If any station that receives the token has no data to send, it simply passes the token to the next station in the ring.

## Slide 36: Channelization Protocol
Channelization is a multiple access method in which the available bandwidth of a link is shared in time, frequency or code between different stations.
There are three basic channelization protocols:
  Frequency Division Multiple Access (FDMA)
  Time Division Multiple Access (TDMA)
  Code Division Multiple Access (CDMA)

## Slide 37: FDMA
In FDMA, the available bandwidth is divided into frequency
bands.
Each station is allocated a band to send its data.
This band is reserved for that station for all the time.
The frequency bands of different stations are separated by small bands of unused frequency.
These unused bands are called guard bands that prevent
station interferences.
FDMA is different from FDM (Frequency Division Multiplexing).
FDM is a physical layer technique, whereas, FDMA is an
access method in the data link layer.

## Slide 39: TDMA
In TDMA, the bandwidth of channel is divided among various
stations on the basis of time.
Each station is allocated a time slot during which it can send its data.
Each station must know the beginning of its time slot.
TDMA requires synchronization between different stations.
Synchronization is achieved by using some synchronization
bits at the beginning of each slot.
TDMA is also different from TDM. TDM is a physical layer technique, whereas, TDMA is an access method in data link layer.

## Slide 41: CDMA
Unlike TDMA, in CDMA all stations can transmit data simultaneously.
CDMA allows each station to transmit over the entire frequency spectrum all the time.
Multiple simultaneous transmissions are separated using coding theory.
In CDMA, each user is given a unique code sequence.

## Slide 42: Working of CDMA
Let us assume that we have four stations: 1, 2, 3 and 4 that are connected to the same channel.
The data from station 1 is d1, from station 2 is d2 and so on.
The code assigned to station 1 is c1, station 2 is c2 and so on.
These assigned codes have two properties:
  If we multiply each code by another, we get 0.
  If we multiply each code by itself, we get 4, (no. of stations).

## Slide 43: Working of CDMA
 When these four stations send data on the same channel, then station 1 multiplies its data by its code
i.e. d1.c1, station 2 multiplies its data by its code i.e. d2.c2 and so on.
The data that goes on the channel is the sum of all these terms:
d1.c1 + d2.c2 + d3.c3 + d4.c4
Any station that wants to receive data from the channel multiplies the data on the channel by the code of the sender.

## Slide 44: Working of CDMA
For e.g.: suppose station 2 wants to receive data from station1.
It multiplies the data on the channel by c1, (code of station 1).
Because (c1.c1) is 4, but (c2.c1), (c3.c1) and (c4.c1) are all 0s, station 2 divides the result by 4 to get the data from station 1.
data
= (d1.c1 + d2.c2 + d3.c3 + d4.c4).c1
= d1.c1.c1 + d2.c2.c1+ d3.c3.c1+ d4.c4.c1
= d1.4 + 0 + 0 + 0
= (d1.4) / 4 = d1

## Slide 45: Working of CDMA
The code assigned to each station is a sequence of numbers called chips.
These chips are called orthogonal sequences.
Each sequence is made of N elements, where N is the number of stations.
[ +1 +1 +1 +1]
[ +1 -1 +1 -1]
[ +1 +1 -1 -1]
[ +1 -1 -1 +1]
c1
c2
c3
c4

## Slide 46: Working of CDMA
This sequence has following properties:
  If we multiply two equal sequences, element by element, and add the result, we get N, where N is the number of elements in the sequence.
  This is called inner product of two equal sequence. [+1 +1 -1 -1] . [+1 +1 -1 -1] = 1 + 1 + 1 + 1 = 4
[ +1 +1 +1 +1]
[ +1 -1 +1 -1]
[ +1 +1 -1 -1]
[ +1 -1 -1 +1]
c1
c2 c3
c4

## Slide 47: Working of CDMA
If we multiply two different sequences, element by element, and add the result, we get 0.
This is called inner product of two different sequence.
[+1 +1 -1 -1] . [+1 +1 +1 +1] = 1 + 1 - 1 - 1 = 0
[ +1 +1 +1 +1]
[ +1 -1 +1 -1]
[ +1 +1 -1 -1]
[ +1 -1 -1 +1]
c1
c2 c3
c4